## Slide 1
17th December 2014
Royal Aeronautical Society
TOULOUSE BRANCH
David COOK, I.Eng, FRAeS
Independent Consultant, President RAeS Paris Branch
Please sign the Attendance Sheet
& include your email address if changed from our records
“The Development of Composite Applications
in Commercial Aircraft Engines”

## Slide 2
Royal Aeronautical Society From 1866
Formed by Duke of Argyll & a group of "aerial navigation enthusiasts"
40 years before properly controlled powered flight
Aim was to share technical knowledge –
George Cayley’s experiments and theoretical work started in the 1790s
Wright Brothers used RAeS papers in design work
4 Hamilton Place

## Slide 3
AIRBUS Business Suite – free for members
Royal Aeronautical Society From 1866
Whole building covered by WiFi internet

## Slide 4
Now more 66 branches in 20 countries
Prime aim remains to share knowledge –
Toulouse Branch formed in 1991
Gordon Corps, Airbus Chief Test Pilot, as first Chairman
(application forms online)
Royal Aeronautical Society From 1866

## Slide 5
Royal Aeronautical Society From 1866
“Friend of the Branch”
  Cost : €10 per annum
  Support the Toulouse Branch programme
Students have Free Membership to RAeS London
  Magazine available electronically
  Can pay £13 per year to receive paper copies of magazine
RAeS Members’ Subscriptions Tax Deductable
  Fabrice Coletto & Peter Potocki will explain

## Slide 6
David COOK
1976 - Graduated from N°1 School of Technical Training, RAF Halton,
Phantom FGR2 aircraft and Chinook helicopters
- BAe Civil Aircraft Division, Hatfield Customer Support
BAe146 and BAe125 programmes.
- Joined Snecma in France, Sales for CFM56 in Scandinavia
CFM Vice President International Sales, Nordic Europe and Middle East
Director, Business Development Aircelle – introduced to Composites
2004 – Independent Consultant
2014 – President RAeS Paris Branch

## Slide 7
David COOK
“The Development of Composite Applications
in Commercial Aircraft Engines”

## Slide 8: David Cook, President, ASM Consulting
Advise, Support, Motivate.
A presentation to the
Royal Aeronautical Society,
Toulouse Branch,
17th December 2014.
The development of composite applications in commercial aircraft engines.

## Slide 9
David Cook: a lifetime of working with engines …
Aircraft maintenance technician,
Royal Air Force
Senior Sales Executive,
Safran Group

## Slide 10
Civil
Military
Fixed - wing
Helicopters
Customer Support
Integrated Logistics Support (ILS)
Contractor Logistics Support (CLS)
Aircraft Sales
Piston Engines
Jet Engines
Maintenance
Airliners
Business jets
Military / Government RFPs
Warranty
Spares and Tooling
Maintenance Costs
Training
Aerospace composites
Sales
Repair
Components
Manufacturing
OEM relations
Civil Aircraft Engines
New engine sales
Maintenance
Contracts
MRO
Engine trading
Finance / leasing
Airframer relations
… with a particular interest in composite applications,
Use of composites
in aircraft engines
Ceramics
Casings
Fan blades
Carbon fibre
Ti/Al
Metal / metal

## Slide 11
How to earn a living as a Consultant,
K =
W
M
Knowledge is Power!
Time is Money!
and
but
hence
W
T
P =
M =
W
K
As knowledge (K) tends towards zero money (M) tends towards infinity !

## Slide 12
Contents:
A historical review of the use of composites in aerospace,
The use of composites in commercial aircraft engines,
MRO issues,
The future of composites in aircraft engine design,
Future aircraft concepts

## Slide 13
Composite materials (or composites for short) are engineered materials
made from two or more constituent materials with significantly different physical or chemical properties and which remain separate and distinct on a macroscopic level within the finished structure.
Examples:
Straw and mud bricks
Re-enforced concrete
Source: Wikipedia
Fibre glass
Carbon fibre re-inforced plastics (CFRP)
What is a ‘composite’?
Notes: Matrix with fibre re-inforcement
Orthotropic – strength dependent on the direction of the load (metals – isotropic)
Easy to manufacture (cold molding)
Strength tailored by the size, number, and direction of fibres

## Slide 14
The advantages and disadvantages of organic composites,
Advantages:
Weight savings vs equivalent metal part,
Ease of production?
Corrosion resistance,
Damage tolerance,
Limited consequential damage,
Repairability,
Disadvantages:
Cost (per equivalent metal part),
Temperature resistance,
Electrical insulation,
Inspectability,

## Slide 15
Major aircraft components (1),
1948: Boeing B-36 used fuel cell support panels
made from ‘reinforced plastics’
1953: Sud Aviation Vautour used ‘significant quantities’ of
fibreglass and composite sandwich panels . . .
1974: Boeing F-15 speedbrake made
entirely from carbon composite and tailplane
from boron/epoxy composite
1975: Boeing tests a solid carbon composite
laminate 737-200 stabilator. The programme
was certified in August 1982

## Slide 16
Major aircraft components (2),
Typical CFRP applications for aircraft flight control surfaces and other components
Most commercial aircraft now using composites for non-critical structural components
Composite applications on the A33O

## Slide 17
Beech Starship: first all carbon composite fuselage. EIS 1989
Boeing F18: Carbon composite wing centre box, tail fins and elevators. EIS 1983
Beech Premier 1: first Business Jet with an all composite fuselage, certified in October 2005
Major aircraft structures,

## Slide 18
Major aircraft structures – Boeing 787,
Boeing 787 – the first commercial airliner with composite wings and fuselage
Boeing 787
Boeing 787 fuselage section manufactured by automated fibre placement
Boeing 787 rear fuselage ready for delivery
Boeing 787 fuselage skin with integrally moulded longerons and riveted frames

## Slide 19
Major aircraft structures - Airbus A350 XWB,
Airbus A350 XWB – composite major structures but a slightly different strategy
Airbus A350 XWB
Composite fuselage panel
Composite wing

## Slide 20
The use of composites in aircraft engines …

## Slide 21
1948: Boeing B-36 used fuel cell support panels
made from ‘reinforced plastics’
Early 1970’s: first use of composite parts in nacelles and non-critical engine components.
September 1995: GE90 enters service on Boeing 777 with first use of CFRP fan blades.
Engine applications,
47 years of development

## Slide 22
How an engine works 1.0.1:
A simple turbo-jet engine
Predominantly used in military applications
Turbo-fan engine
Predominantly used in civil applications
Different engine concepts for different performance requirements and aircraft applications

## Slide 23
How an engine works 1.0.2:
Very high rotational speeds (15,000 rpm) and very high temperatures (1,700°c) ensure that many engine parts are safety critical,
Engine design must resolve a number of engineering contradictions:
  Fan and turbine speeds,
  Compressor ratio and surge margin,
  Combustion temperatures and NOx pollution,
  Aircraft noise and engine weight,

## Slide 24
Carbon composite
fan case
Carbon composite
fan blades
3D weave, RTM
Carbon composite
OGVs
Carbon composite
fan frame
Carbon composite
HP compressor
stator vanes
Ti/Al HP compressor
blisks
Ceramic composite
combustor casing
Hot Section casings?
Shafts?
Ti/Al LPT blades
Ceramic composite
HPT nozzles, blades
Ceramic composite
Exhaust plug
Multiple applications for composites already identified,

## Slide 25
Carbon composite outer bypass duct,
M88 composite outer bypass duct saves 4kg (20%) relative to titanium duct
Snecma M88 engine for the Dassault Rafale aircraft

## Slide 26
Components
Component manufacturers looking at composite materials for housings, casings, etc
Potential 25% weight reduction ?
Issues:
  High pressure hydraulic systems (3,000 psi to 5,000 psi),
  Long term porosity resistance,
  All electric NGSA aircraft?
Systems
  Fibre glass and carbon composite low pressure pipes and ducting already in use,
Composite filter
housings
Source: Green Tweed
Composite applications for engine components,
Carbon fibre FADEC housing for Rolls-Royce engine
Source: ASM

## Slide 27
Applications for CFRP materials: CFM LEAP engine family,
Classic high BPR engine architecture,
  Two shafts, direct drive fan,
  12:1 BPR, 45:1 OPR
Incorporates key technology developments vs CFM56,
  Composite ‘3D weave’ RTM fan blade and case,
  Blisks,
  New ceramic temperature-resistant coatings,
Objectives: 16% improvement in fuel burn with reduced noise and emissions,
EIS on A320neo and Comac C919 in 2016, EIS on 737max in 2017,
CFM LEAP fan blade
Photo: CFM

## Slide 28
Demystifying the 3D weave …
Complex weave pattern
CFM LEAP 3D weave fan blade
Photos: ASM
CFM LEAP 3D weave fan case
Photo: ASM
3D weave fibre insert
Photo: ASM

## Slide 29
Metal composites (1),
Silicon fibre
re-inforced aluminium
Source: CMT
Most suitable for high temperature, high stress parts like compressor disks and LP turbine blades
Typical metal composites:
  Titanium/Aluminides (Ti/Al)
  Aluminium, magnesium or titanium
  re-inforced with boron, silicon or carbon fibres
60% weight reduction compared to conventional metal part
Significant (200%?) increase in strength and stiffness

## Slide 30
Metal composites (2): some examples …
CFM LEAP Ti/Al compressor blisk
Photo: CFM
PW6000 compressor blisk
Photo: MTU
CFM LEAP
Al/Ti LP Turbine blade
Photo: CFM

## Slide 31
Ceramics (1),
Most suitable for very high temperature, high stress parts like combustion chambers and HP turbine nozzles
Typical ceramic composites:
  Silicon Carbide reinforced with silicon carbide fibres (SiC/SiC)
  Silicon Carbide reinforced with aluminium filaments (SiC/Al)
50-70% weight reduction compared to equivalent metallic part
Capable of withstanding +1,300°c without cooling
No cooling system = less weight and complexity, increased reliability
  full use of ceramics in LEAP engine could save 175 lbs per engine
No cooling air = less NOx
Tough and shock
resistant!

## Slide 32
Ceramics (2): some examples …
Prototype ceramic combustion chamber.
Photo: GE
Snecma prototype A340 ceramic exhaust nozzle.
Photo: ASM
Snecma prototype ceramic exhaust plug. Photo: ASM
LEAP ceramic HPT shrouds. Photo: CFM
Prototype ceramic HPT nozzle.
Photo: GE

## Slide 33
MRO issues

## Slide 34
Composite fan blade maintenance,
GE90-115B
128 ins fan diameter
22 blades
1,019 lbs fan weight
CFM56-7B
61 ins fan diameter
24 blades
260 lbs fan weight
LEAP-X
71 ins fan diameter
18 blades
168 lbs fan weight
Traditional metal blades are resistant to damage and easily repairable
Large diameter, slow turning composite fan blades avoid damage and rarely need repairing
High speed 3D weave composite blades may not be so resistant to damage, will be difficult to repair (if at all) but may be replaced singly

## Slide 35
Compressor blades repair - blisks,
Future
Traditional
Blades accessed by opening up Top Case,
Blades are free on the disk:
  Minor defects rectified by in-situ grinding,
  Major defects rectified by individual blade replacement,
Blades accessed by module breakdown,
Blades are integral part of the blisk:
  Minor defects rectified by repair on removed blisk,
  Major defects rectified by blisk replacement,
ASM photo of MTU display

## Slide 36
Self-healing composites,
Ceramics can ‘self-heal’ when the penetration of oxygen into a crack provokes oxidisation of a glassy ‘fuse’ which stops crack progression,
Carbon fibre composites can recover 75% of their original strength using self-healing repair techniques,

## Slide 37
The future of composites in aircraft engine design

## Slide 38
Future composite applications,
CFRP use expected to FALL in future generations of civil aircraft
Modern aircraft use high percentages of composites – but will this situation last?

## Slide 39
Cost:
  Carbon fiber and resins are products derived from oil – and we expect the price of oil to
  rise,
  Increasing costs of production,
Revenge of the metals:
  If 53% of A350 is CFRP then 47% is still metal!
  Metals have reacted to CFRP popularity by getting cheaper – esp Titanium,
  New alloys (Al/Li, Al/Mg) are lighter than CFRP – and cheaper,
  Metals are cheaper to manufacture into complex shapes,
    Additive Manufacturing,
Aircraft manufacturers commercial strategy is changing:
  Order books are full,
  Only way to make more money is to improve margins,
  Manufacturers paying less for weight advantage,
Proportion of composites used in aircraft structures will fall as oil prices rise and alternatives emerge
Reasons for composites likely fall from favour,

## Slide 40
Composite manufacture: a costly and complex process?
Many complex CFRP structures are laid-up by hand
‘Clean Room’ facilities often required to meet aerospace quality requirements
Automation only suitable for large, regular shapes
Autoclave curing is expensive, time-consuming, and risky
The manufacture of composite parts for the aerospace industry is labour intensive, expensive, and time-consuming

## Slide 41
Challenges facing the increased use of CFRP in engines,
100°c
200°c
300°c
400°c
Avimid
N
COST!
6,000 hrs
30,000 hrs
Epoxy
BMI
Avimid
R
PMR
15
Source: Cytec
Prototype HP
compressor stators
Source: Snecma
A prototype composite fan frame
Photo: ASM
Operating
Temperature
Increased operating temperatures,
Increasingly complex structures,
High volume, cost effective production with acceptable quality and repeatability.
Use of composites remain a high-cost option for improving engine efficiency

## Slide 42
Carbon composites used in aircraft engines was1.49 million lbs in 2007,
This represented a market value at the time of $400-450m,
Demand for carbon composites to be used in aircraft engines is expected
to exceed nearly 3 million lbs by 2016,
Value of carbon composites consumed by engines during this 10 year
period is expected to be around $7-8 bn,
But composite demand for engines is expected to remain high …
Source: ‘Aviation Outlook Report 2008

## Slide 43
Design:
  Ensuring optimum ply lay-up for high stress components,
  Ensuring optimum mold design for complex shapes,
Materials:
  New resins and fibers for greater temperatures / greater strength / greater fatigue resistance,
  Develop materials which lend themselves to industrial manufacturing processes,
Manufacturing:
  Ability to transform increasingly sophisticated CAD designs into workable production programmes,
  Develop more cost-effective industrial manufacturing processes,
Challenges facing the increased use of carbon composites,

## Slide 44
Design
  Increasingly sophisticated CAD programmes to determine ply layup in 3D aero, highly stressed engine components,
  Sophisticated flow simulation software to ensure correct moulding of complex parts,
Simulation of resin flow in a complex RTM mold
Source: Snecma
Prediction of dry spots in an RTM molded aerofoil
using ‘Polyworx’ software.
Source: Polyworx
Ply orientation simulation
for aerofoil
Source: Snecma
Design challenges:

## Slide 45
Develop materials which lend themselves to industrial manufacturing processes:
  Chopped fibre filler for complex RTM molding,
  ‘non-stick’ resins which facilitate tape layup,
Resin Transfer Molding process
Source: JHM Technologies
Tape lay-up by machine
Materials challenges:

## Slide 46
Carbon Nanotubes (CNT): the wonder material for the future?
First discovered in 1991,
Cylindrical carbon molecules with a l/d ratio greater than
1,000,000,
Exhibit extra-ordinary mechanical properties such as
strength, stiffness, conductivity, flame resistance, wear
resistance, …..
Experiments with CNTs as bulk filler in resin matrix,
Potential engine applications:
  structures,
  thermal barrier coatings,
  high temperature sensors,
Issues:
  Ability to bond with matrix and transfer stress,
  Uniform distribution and alignment of filaments within the matrix,
  Cost currently prohibitive - $1,000 / gm,

## Slide 47: Nanotube strength capability:
Tensile strength = 63 gigapascals !

## Slide 48
Manufacturing,
Manufacturing
  Ability to transform increasingly sophisticated CAD designs into workable production programmes,
  Develop cheaper manufacturing processes:
    ‘Quickstep’ hot oil curing eliminates autoclave,
  Achieve high volume production to meet production ramp-up with very high levels of quality,

## Slide 49
Future engine concepts

## Slide 50
Open Rotor Concepts – geared or ungeared?
Two concepts currently being developed:
  Rolls-Royce geared counter-rotating rotor system,
  Snecma direct-drive counter-rotating rotor system,
Similar objectives:
  25 to 30% reduction in fuel burn relative to today’s technology
  engines,
  similar reductions in CO2 levels,
Expected EIS – 2025 to 2030?
Challenges:
  Noise,
  Complexity,
But the ‘Open Rotor’ already exists! Antonov 70 first flew in 1994,
Open Rotor - an expensive ‘knee jerk’ reaction to high fuel prices?
Notes: Antonov 70 first flight – December 1994
4 x Ivchenko Progress D27 direct drive Open Rotor engines.

## Slide 51
Ultra High Bypass ratio engines,
Ultra-high Bypass ratio (UHBPR) engines use
a more conventional architecture,
  Simple layout,
  Next-generation materials,
  Large diameter fan driven by gearbox,
  Reverser pitch change mechanism in the fan,
BPR of < 25:1 will achieve significant fuel burn
reductions,
Rolls-Royce have already unveiled their
geared ‘Ultra-Fan’ concept for EIS 2030,
GE have recently unveiled a ‘hybrid’ concept,
  UHBPR engine,
  Electric motor on LP shaft,
  HP core is run at idle, or even shut down,
  in cruise,
UHBPR geared fan engines – a much more credible option for high thrust engine development (IMHO)

## Slide 52
More electric – or all electric – aeroplanes?
Boeing 787 is the first aircraft with a ‘no bleed’ powerplant
  Electrically driven Air Conditioning systems takes 35% less power from engines than
  conventional system
  Electrically driven hydraulic pumps with one engine-driven pump as back-up
  2,000 lbs weight saving
  3% fuel burn improvement
  1,400 Kva generation capability
Fly-by-wire’ flight controls,
Electric brakes and engine controls,
Elimination of high pressure air bleeds from engines produces significant efficiency improvements

## Slide 53
Towards the ‘All Electric’ aircraft?
Airbus ‘E-Fan’ currently under flight test
Electroflight racer concept currently being developed in UK
Airbus and Boeing studying various concepts
A number of concepts are being studied but energy storage considerations are critical to commercial success

## Slide 54
The Airbus ‘e-concept’ aircraft
Distributed propulsion system uses a gas turbine as a source of electrical power to drive propulsion fans and all the other aircraft systems
‘Hybrid’ is the new buzzword in the aerospace industry!
Electrically driven fans integrated into the structure of the aircraft

## Slide 55
Conclusions:
Carbon fibre composites have an established place in aerospace design bringing a significant number of advantages and some inconveniences,
While carbon fibre usage in aircraft structures may diminish in the future it will remain a key feature of engine design,
New composite materials will continue to be developed to respond to the aircraft engine’s unique design and operational requirements,
Continued attention will need to be paid to MRO and manufacturing processes to keep production and maintenance costs low,
New aircraft propulsion concepts will continue to ensure that materials development will be at the forefront of engine research,

## Slide 56
Thank you for your attention.
asmcontact@aol.com
+33 6 1135 4330

## Slide 59
Forthcoming Programme
www.RAeS-Toulouse.org
and links to
For posters / any changes / updates
www.Academie-Air-Espace.com
AAAf-MP@sfr.fr

## Slide 60
Frohes Fest und ein gutes Neues Jahr
Merry Christmas and Happy New Year
Bonnes Fêtes / Meilleurs Voeux
Feliz Navidad & Feliz Aňo Nuevo
God Jul och Gott Nytt År